## Slide 1: DVM Proposal
Integrating Bench Measurements into SIMetrix/SIMPLIS DVM
5/15/17 – Version 1.0
Chris Bridge, SIMPLIS Technologies

## Slide 2: DVM Basics
DVM simulates a single schematic, using a testplan file which defines the test conditions and measurements to be made during each simulation. An archival report is generated with the graphical, scalar and PASS/FAIL status of each test.
DVM allows users to run SIMetrix scripts before and after the simulation run. What can be accomplished in these scripts is almost unlimited. This is where we would import bench measurement data.
For example, a post process script could read bench waveform data from disk, process it, plot that data on a graph, and make measurements on the waveforms. A second script could make comparisons between the bench data and the design specifications, and flag the test as a PASS or FAIL based on the design specifications.
All data, whether read from disk, or generated from a simulation is included in the report, as if the data were generated during a simulation run.

## Slide 3: Data Import Concepts (1 of 3)
The post process script will run after each test, and before DVM saves the graphs and scalar measurements for that test.
The post process script needs to be generic in nature – the same script will run after each test, and will load data if it is available, process that data (plotting, measurements, etc.) according to some rules.
If no data is available, then the post process script will exit and the next test will be executed.
Note that all lab/bench data must be saved to disk before the testplan is run on the schematic. You can run single tests out of the testplan for debugging purposes.

## Slide 4: Data Import Concepts (2 of 3)
In order to make the post process script as general purpose as possible, the bench data needs to be organized in a way for the script to find it.
A proposed data directory structure mimics the label property of a test, which is defined in the testplan:
  Testplan label: AC Analysis|Bode Plot|VIN Nominal|100% Load
  Loads data from a directory: IMPORT_DIR/AC Analysis/Bode Plot/VIN Nominal/100% Load
  IMPORT_DIR is a immediate subdirectory of the DVM test schematic. We store the value of IMPORT_DIR on the DVM Control symbol as a property. The script can read this data as well as the current testplan label to find the directory containing the bench data for this test.

## Slide 5: Data Import Concepts (3 of 3)
Multiple sets of bench data can be saved to disk in different IMPORT_DIR directories.
By saving IMPORT_DIR on the DVM control symbol as a property, any set of data can be used in the comparison to simulation data. The user only needs to change the value of the DVM Control Symbol’s IMPORT_DIR property, and run the DVM testplan.

## Slide 6: Post Process Script(s)
At this point, the post process script knows the file directory where the bench data is stored.
How does the post process script know what to do with the bench data, for example, how does it know what files contain waveform data, and how does the script know what to do with that data?
Some form of interface layer should be used to tell the postprocess script what data is present and how to process that data.
Next slide: An Example

## Slide 7: Post Process Script to Load Bench Data From Disk; Generate Specification Checking
Example: A Bode Plot waveform representing the overall control loop response of the converter is taken in the lab and saved as ASCII data. We desire the following behavior:
  Plot the bench data for the bode plot gain/phase on the same graph as the simulation bode plot gain/phase, in a specified color.
  Make measurements on both simulation and bench data:
    Gain Margin
    Phase Margin
    Gain Crossover Frequency
  Compare both the simulation data and the bench data for these measurements to specification values and issue a PASS or FAIL status.

## Slide 8: Two Script Approach - Definitions
First script (import_data.sxscr, processes actions in IMPORT_FILENAME):
  Loads data from disk,
  Plots data,
  Makes measurements.
Second Script (check_specs.sxscr, processes specs in SPECS_FILENAME):
  Loads specification data from disk
  Reads measurements on graphs
  Makes comparison of spec to measurement
  Returns PASS/FAIL status

## Slide 9: Data Files - Definitions
IMPORT_FILENAME = import.txt:
  Defines data files to load from disk,
  Defines curves to be plotted from those data files,
  Makes measurements on those curves.
SPECS_FILENAME = design_specs.txt:
  Defines specification based on measurements
  Min/Max Spec values for each measurement
  Includes pass/fail specification information for each measurement

## Slide 10: Three Special Symbol Properties:
IMPORT_DIR
  Defines directory which holds the data to load from disk. Both IMPORT_FILENAME and SPECS_FILENAME files are expected to reside in this directory
IMPORT_FILENAME
  Defines the filename in IMPORT_DIR directory w/ instructions for data import
SPECS_FILENAME
  Defines the filename for the design specifications file in the IMPORT_DIR directory

## Slide 11: Summary
A simple system involving two general purpose scripts which:
  Import data from disk and make measurements on that data
  Check specifications on both simulation and bench data
Once data is imported, plotted, measured and specifications are made, these data are saved into the report, just as if the data came from the simulation.
Two data files are needed:
  An “import” file which defines the data to load, how to plot it, and what measurements to make.
  A “specs” file containing the design specifications
The resulting report has both bench and simulation waveforms, measurements made on those waveforms, and each test is given a PASS/FAIL status based on the design specifications. This report is archival and can be zipped and saved for future reference.
If, at some time in the future, new bench data becomes available, that data can be saved in a new IMPORT_DIR directory and the test suite can be run on that data.